## Slide 1: Using QLab with Eos
Jim Uphoff and Hans Hinrichsen

## Slide 2: Let’s Play!

## Slide 3: Game Elements
Score Keeping
  IR Sensor
  iPad
Gameplay Actions
  Microphone – Sound2Light
  Shotbox
Ambience
  Pre/post music and lights
  OSC triggered, MIDI Time Code synchronized

## Slide 4: Riser
DMX
DMX
Audio
USB
OSC (Net)
OSC (Net)
ACN (Net)
OSC (Net)
ACN, OSC (Net)
USB
MIDI
OSC (Net)
Audio
OSC
IR Sensor
Notes: Walk through riser, step by step building system

## Slide 5: Protocols
MIDI – MIDI Time Code
OSC - Open Sound Control
  IP Recap
  Messages – Address Patterns and Arguments
  UDP vs TCP
  OSC v1.0 vs v1.1

## Slide 6: MIDI Time Code
Representation of time over MIDI
  hh:mm:ss:ff (Hours, Minutes, Seconds, Frames)
  24, 25, 29.97, 30 frames
Used to synchronize devices
Carries no other “meaningful” information – is only a synchronization method
Internal vs external timecode
  Freewheeling

## Slide 7: OSC – Network Setup
Wired Network
  Everything must be in a compatible subnet
  ETC default: 10.101.x.x or 10.101.0.0/16

## Slide 8: OSC – Wireless Setup
Wireless Network
  Using a wireless router, connected to WAN port
  Router WAN port – 10.101.125.1
  Router LAN subnet – 192.168.1.0/24
  Router provides DHCP server
Router filters data we don’t want on the wireless link
Router still passes OSC to console

## Slide 9: OSC – UDP vs TCP
IP: UDP vs TCP
  User Datagram Protocol
    Stateless – no “connection”
    Does not guarantee message reaches destination
  Transmission Control Protocol
    Direct connection
    Guaranteed delivery
    Two OSC versions – 1.0 (packet length) and 1.1 (SLIP)
      Must match for two devices to talk to each other!
IP: Ports
  An endpoint or “mailbox” associated with an IP address
  10.101.2.177:53000

## Slide 10: OSC Messages
Address Pattern and Arguments
  Pattern – command
  Arguments – information to supplement command
Arguments vary based on platform used to send them!
TouchOSC
Eos Magic Sheets
OSCWidgets

## Slide 11: Message Examples
QLab
  /cue/1/start
  /cue/1/stop
Eos
  /eos/cue/1/1/fire
  /eos/macro/11/fire
  /eos/user=1
  /eos/sc/game_start (Event List!)

## Slide 12: Elements
UDP OSC
  Ion Console
  TouchOSC on an iPad
  Raspberry Pi (Raspbian) with Python code
  MacBook Pro and QLab

## Slide 13: OSC: UDP
Setup - General
  Specify send and receive ports
  Remember that send on one device needs to match receive on the other
  Specify transmit IP address (IP of device that is receiving the UDP OSC)

## Slide 14: Elements
TCP OSC (1.1)
  Ion Console
  PC running Sound2Light
  PC running OSCWidgets
  QLab
Eos
  TCP Port 3032
  Configurable between v1.0 (packet length) and v1.1 OSC (SLIP)
QLab
  TCP Port 53000
  SLIP (v1.1) only
Eos and QLab cannot directly connect via TCP – both “servers”

## Slide 15: Game Elements - Configuration
Score Keeping
  IR Sensor
  iPad
Gameplay Actions
  Microphone – Sound2Light
  Shotbox
Ambience
  Pre/post music and lights
  OSC triggered, MIDI Time Code synchronized

## Slide 16: IR Sensor
Adafruit 2167 IR Sensor
  https://www.adafruit.com/product/2167
Raspberry Pi
  https://www.raspberrypi.org/downloads/raspbian/
Python3
Osc4py3 library
  http://osc4py3.readthedocs.io

## Slide 17: Eos: Show Control List Messages
Define an OSC input that describes action
Implementation can change without rewriting OSC device’s mapping
/eos/sc/player1_plus1
  Runs Macro 1002
    Press Go on Cue List 11

## Slide 18: Showfiles and Code
Showfiles
  https://github.com/hinrichsenhans/cue2017
PiBags
  https://github.com/hinrichsenhans/pibags